CANopen

Introduction
CANopen Protocol
DO
These are dictionary objects. They are used for storing settings of the node.
- Index: Unsigned 16-bit number
- Sub index: Unsigned 8-bit number
- Object name: Name of the object
- Data type: Array, U8, U16, U32
- Access: Read, Write, Read-Write
- PDO mapping: Receive, Transmit

Notice that the DO can be split into these areas:
- Reserved area (Index: 0x0)
- Data types area (Index: 0x1 – 0x25F)
- Reserved area (Index: 0x260 – 0xFFF)
- Communication parameter area (Index: 0x1000 – 0x1FFF)
- Manufacturer parameter area (Index: 0x2000 – 0x5FFF)
- Application parameter area (Index: 0x6000 – 0x9FFF)
- Interface parameter area (Index: 0xA000 – 0xBFFF)
- Reserved area (Index: 0xC000 – 0xFFFF)

Where Communication parameter area can be split into these areas:
- General communication objects area (Index: 0x1000 – 0x1029)
- SDO Parameter objects area (Index: 0x1200 – 0x12FF)
- CANopen Save objects area (Index: 0x1300 – 0x13FF)
- PDO Parameter objects area (Index: 0x1400 – 0x1BFF)
- SDO Manager objects area (Index: 0x1F00 – 0x1F11)
- Configuration Manager objects area (Index: 0x1F20 – 0x1F27)
- Program control objects area (Index: 0x1F50 – 0x1F54)
- NMT Master objects area (Index: 0x1F80 – 0x1F89)

Index	Sub index	Object name	Data type	Access	PDO mapping
0x1000	0x0	Device type	U32	Read	-
0x1001	0x0	Error register	U8	Read	-
0x1002	0x0	Calibration date	U32	Read
0x1003		Pre-defined error field	Arrary
	0x0	Number of errors	U8	Read Write
	0x1	Last error	U32	Read
	0x2-0xF	Older error	U32	Read
0x1005	0x0	COB-ID SYNC	U8	Read Write
0x1008	0x0	Device name	U32	Read
0x1009	0x0	Hardware version	U32	Read
0x100A	0x0	Software version	U32	Read
0x100C	0x0	Guard time ms	U16	Read Write
0x100D	0x0	Life factor	U8	Read Write
0x1010		Save parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	All	U8	Read Write
	0x2	Communication	U8	Read Write
	0x3	Application	U8	Read Write
	0x4	Manufacturer	U8	Read Write
0x1011		Restore parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	All	U8	Read Write
	0x2	Communication	U8	Read Write
	0x3	Application	U8	Read Write
	0x4	Manufacturer	U8	Read Write
0x1014	0x0	COB ID emergency message	U32	Read
0x1015	0x0	Inhibit time ms between two EMCY messages	U16	Read Write
0x1017	0x0	Heartbeat interval ms	U16	Read Write
0x1018		Identity object	Arrary
	0x0	Highest sub index	U8	Read
	0x1	Vendor ID	U32	Read Write
	0x2	Product code	U32	Read Write
	0x3	Revision number	U32	Read Write
	0x4	Serial number	U32	Read Write
	0x5	Node ID	U8	Read Write
0x1200		Server SDO parameters	Arrary
	0x0	Highest sub index	U8	Read
	0x1	COB ID client > server	U32	Read Write
	0x2	COB ID server > client	U32	Read Write
0x1800		Transmit PDO1 communication	Arrary
	0x0	Highest sub index	U8	Read
	0x1	COB-ID	U32	Read Write
	0x2	Transmission type (synchronous, asynchronous, manufacturer specific)	U8	Read Write
	0x3	Inhibit time between two Transmit PDO messages	U16	Read Write
	0x4	Compatibility entry	U8	Read Write
	0x5	Event Timer (multiple of 1 ms, 0 deactivated)	U16	Read Write
0x1801		Transmit PDO2 communication	Arrary
	0x0	Highest sub index	U8	Read
	0x1	COB-ID	U32	Read Write
	0x2	Transmission type (synchronous, asynchronous, manufacturer specific)	U8	Read Write
	0x3	Inhibit time between two Transmit PDO messages	U16	Read Write
	0x4	Compatibility entry	U8	Read Write
	0x5	Event Timer (multiple of 1 ms, 0 deactivated)	U16	Read Write
0x1802		Transmit PDO3 communication	Arrary
	0x0	Highest sub index	U8	Read
	0x1	COB-ID	U32	Read Write
	0x2	Transmission type (synchronous, asynchronous, manufacturer specific)	U8	Read Write
	0x3	Inhibit time between two Transmit PDO messages	U16	Read Write
	0x4	Compatibility entry	U8	Read Write
	0x5	Event Timer (multiple of 1 ms, 0 deactivated)	U16	Read Write
0x1803		Transmit PDO4 communication	Arrary
	0x0	Highest sub index	U8	Read
	0x1	COB-ID	U32	Read Write
	0x2	Transmission type (synchronous, asynchronous, manufacturer specific)	U8	Read Write
	0x3	Inhibit time between two Transmit PDO messages	U16	Read Write
	0x4	Compatibility entry	U8	Read Write
	0x5	Event Timer (multiple of 1 ms, 0 deactivated)	U16	Read Write
0x1A00		Transmit PDO1 mapping parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	Mapping entry 1, both types: TMS / TMM	U32	Read Write
	0x2	Mapping entry 2, type: TMS / TMM	U32	Read Write
	0x3	Mapping entry 3	U32	Read Write
	0x4	Mapping entry 4	U32	Read Write
	0x5	Mapping entry 5	U32	Read Write
	0x6	Mapping entry 6	U32	Read Write
	0x7	Mapping entry 7	U32	Read Write
	0x8	Mapping entry 8	U32	Read Write
0x1A01		Transmit PDO2 mapping parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	Mapping entry 1, both types: TMS / TMM	U32	Read Write
	0x2	Mapping entry 2, type: TMS / TMM	U32	Read Write
	0x3	Mapping entry 3	U32	Read Write
	0x4	Mapping entry 4	U32	Read Write
	0x5	Mapping entry 5	U32	Read Write
	0x6	Mapping entry 6	U32	Read Write
	0x7	Mapping entry 7	U32	Read Write
	0x8	Mapping entry 8	U32	Read Write
0x1A02		Transmit PDO3 mapping parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	Mapping entry 1, both types: TMS / TMM	U32	Read Write
	0x2	Mapping entry 2, type: TMS / TMM	U32	Read Write
	0x3	Mapping entry 3	U32	Read Write
	0x4	Mapping entry 4	U32	Read Write
	0x5	Mapping entry 5	U32	Read Write
	0x6	Mapping entry 6	U32	Read Write
	0x7	Mapping entry 7	U32	Read Write
	0x8	Mapping entry 8	U32	Read Write
0x1A03		Transmit PDO4 mapping parameters	Array
	0x0	Highest sub index	U8	Read
	0x1	Mapping entry 1, both types: TMS / TMM	U32	Read Write
	0x2	Mapping entry 2, type: TMS / TMM	U32	Read Write
	0x3	Mapping entry 3	U32	Read Write
	0x4	Mapping entry 4	U32	Read Write
	0x5	Mapping entry 5	U32	Read Write
	0x6	Mapping entry 6	U32	Read Write
	0x7	Mapping entry 7	U32	Read Write
	0x8	Mapping entry 8	U32	Read Write
0x1F50		Program data write
	0x0	Highest sub index	U8	Read
	0x1	Data 1	U8	Write
	0x2	Data 2	U8	Write
	0x4	Data 3	U8	Write
0x1F51		Program data control
	0x0	Highest sub index	U8	Read
	0x1	Data 1	U8	Read Write
	0x2	Data 2	U8	Read Write
	0x4	Data 3	U8	Read Write

SDO
This is used if the transmitter wants to send something to the receiver. When the transmitter sends a SDO object to the receiver, then the receiver responds with a SDO object as well.

Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x580 + Node ID	CS	Index LSB / Index MBS		Sub index	Data

Receive command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x600 + Node ID	CS	Index LSB / Index MBS		Sub index	Data

Type	Enum in C code	Hex	Meaning
CS	CS_SDO_READ_DICTIONARY_OBJECT	0x40	Read DO object and send back

C functions:
void CANopen_Transmit_SDO_Transmit_SDO_Object(CANopen *canopen, uint8_t cs, uint16_t index, uint8_t sub_index, uint8_t data[]);

PDO
This is used if the transmitter wants to send something to the receiver. There are 4 different PDOs and TPDO1 transmit so another RPDO1 can receive that message.
PDO1
Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x180 + Node ID	Data

Receive command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x200 + Node ID	Data

PDO2
Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x280 + Node ID	Data

Receive command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x300 + Node ID	Data

PDO3
Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x380 + Node ID	Data

Receive command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x400 + Node ID	Data

PDO4
Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x480 + Node ID	Data

Receive command:
COB ID	Byte 0
0x500 + Node ID	Data

C functions:
void CANopen_Transmit_PDO_Transmit_PDO1_Object(CANopen *canopen, uint8_t node_id, uint8_t data[]); / void CANopen_Transmit_PDO_Transmit_PDO1_Object(CANopen *canopen, uint8_t node_id, uint8_t data[]); / void CANopen_Transmit_PDO_Transmit_PDO1_Object(CANopen *canopen, uint8_t node_id, uint8_t data[]); / void CANopen_Transmit_PDO_Transmit_PDO1_Object(CANopen *canopen, uint8_t node_id, uint8_t data[]);

TIME
This is used when the slaves wants to send the time stamp to the master. The milliseconds are the counting time from midnight. For example 00:15, which is 15 minutes, then the counting of milliseconds will be 1000 * 60 * 15 = 900000 = 0xDBBA0. Days are the counting days from January 1, 1984. It will overflow on June 7, 2163.

TODO: Ska detta vara en producer?

Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	Milliseconds LSB Milliseconds MBS				Days LSB / Days MSB		0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	TIME_SLAVE_TO_MASTER	0x100	Transmit from slave to master

EMCY
This is used if the producer wants to broadcast an error message to the consumers. An EMCY will save the information in the OD:
- Error code will be saved in OD_INDEX_PRE_DEFINED_ERROR_FIELD
- Error register will be saved in OD_INDEX_ERROR_REGISTER
- COB ID will be saved in OD_INDEX_COB_ID_EMERGENCY_MESSAGE

The OD_INDEX_PRE_DEFINED_ERROR_FIELD can be saved up to OD_SUB_INDEX_15 times where the OD_SUB_INDEX_0 describes how many errors there are. Writing zero to OD_SUB_INDEX_0, clears the error list.

Att göra:
Gör en funktion som tömmer felmeddelanden. SDO.

Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x80 + Node ID	Error code LSB / Error code MSB		Error register	Vendor specific data

Enum	Hex	Meaning
ERROR_CODE_NO_ERROR	0x0000	No Error
ERROR_CODE_GENERIC_ERROR	0x1000	Generic Error
ERROR_CODE_CURRENT	0x2000	Current
ERROR_CODE_CURRENT_INPUT_SIDE	0x2100	Current input side device
ERROR_CODE_CURRENT_DEVICE	0x2200	Current inside the device
ERROR_CODE_CURRENT_OUTUT_SIDE	0x2300	Current device output side
ERROR_CODE_VOLTAGE	0x3000	Voltage
ERROR_CODE_MAINS_VOLTAGE	0x3100	Mains Voltage
ERROR_CODE_VOLTAGE_DEVICE	0x3200	Voltage inside the device
ERROR_CODE_OUTPUT_VOLTAGE	0x3300	Output Voltage
ERROR_CODE_TEMPERATURE	0x4000	Temperature
ERROR_CODE_AMBIENT_TEMPERATURE	0x4100	Ambient Temperature
ERROR_CODE_DEVICE_TEMPERATURE	0x4200	Device Temperature
ERROR_CODE_DEVICE_HARDWARE	0x5000	Device Hardware
ERROR_CODE_DEVICE_SOFTWARE	0x6000	Device Software
ERROR_CODE_INTERNAL_SOFTWARE	0x6100	Internal Software
ERROR_CODE_USER_SOFTWARE	0x6200	User Software
ERROR_CODE_DATA_SET	0x6300	Data Set
ERROR_CODE_ADDITIONAL_MODULES	0x7000	Additional Modules
ERROR_CODE_MONITORING	0x8000	Monitoring
ERROR_CODE_COMMUNICATION	0x8100	Communication
ERROR_CODE_CAN_OVERRUN	0x8110	CAN Overrun (Objects lost)
ERROR_CODE_CAN_PASSIVE_MODE	0x8120	CAN in Error Passive Mode
ERROR_CODE_GUARD_HARTBEAT	0x8130	Guard Error or Heartbeat Error
ERROR_CODE_RECOVER_FROM_BUS	0x8140	Recovered from bus off
ERROR_CODE_CAN_ID_COLLISION	0x8150	CAN-ID collision
ERROR_CODE_PROTOCOL_ERROR	0x8200	Protocol Error
ERROR_CODE_PDO_LENGTH	0x8210	PDO error due to length
ERROR_CODE_PDO_TO_LONG	0x8220	PDO length exceeded
ERROR_CODE_DAM_MPDO_NOT_PROCEED	0x8230	DAM MPDO not processed
ERROR_CODE_SYNC_DATA_LENGTH	0x8240	Unexpected SYNC data length
ERROR_CODE_RECEIVE_PDO_TIMEOUT	0x8250	Receive PDO timeout
ERROR_CODE_EXTERNAL_ERROR	0x9000	External Error
ERROR_CODE_ADDITIONAL_FUNCTIONS	0xF000	Additional Functions
ERROR_CODE_DEVICE_SPECIFIC	0xFF00	Device specific

Bit	Enum in C code	Hex
Bit 7	ERROR_REGISTER_MANUFACTURER_SPECIFIC	0x80
Bit 6	ERROR_REGISTER_BIT_6_RESERVED	0x0
Bit 5	ERROR_REGISTER_DEVICE_PROFILE_SPECIFIC	0x20
Bit 4	ERROR_REGISTER_COMMUNICATION_ERROR	0x10
Bit 3	ERROR_REGISTER_TEMPERATURE_ERROR	0x8
Bit 2	ERROR_REGISTER_VOLTAGE_ERROR	0x4
Bit 1	ERROR_REGISTER_CURRENT_ERROR	0x2
Bit 0	ERROR_REGISTER_GENERIC_ERROR	0x1

C functions:
STATUS_CODE CANopen_Producer_EMCY_Transmit_Error_Message(CANopen *canopen, uint16_t error_code, uint8_t error_register, uint8_t vendor_specific_data[]); / STATUS_CODE CANopen_Consumer_EMCY_Receive_Error_Message(CANopen *canopen, uint8_t node_ID, uint8_t data[]);

SYNC
This is used if the master wants to transmit a SYNC command to a slave.

Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	0x0	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	SYNC_MASTER_TO_SLAVE	0x80	Transmit from master to slave

C functions:
void CANopen_Master_SYNC_Transmit_Synchronization(CANopen *canopen);

HEARTBEAT
This is used if the producer will broadcast status operations to consumers. Hartbeat should be transmitted out from every slave in a cyclic period e.g 1000 ms. If the cyclic period is zero, then heartbeat will be disabled. Heartbeat will also be disabled at the start up process of the controller.

Att göra:
- När man sätter heartbeat intervalltid, så aktiveras heartbeat och gurad avaktiveras
- När node är vid uppstart, så ska heartbeat och gurard vara avaktiverade
Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x700 + Node ID	Status	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Status	Enum in C code	Hex	Meaning
Bit 7	TOGGLE_HEARTBEAT_0	0x0	Bit changes for every time the C function calls
Bit 7	TOGGLE_HEARTBEAT_1	0x1	Bit changes for every time the C function calls
Bit 6..0	STATUS_OPERATIONAL_ENTER_PRE_OPERATIONAL	0x7F	Node has enter Pre-Operational mode
Bit 6..0	STATUS_OPERATIONAL_NORMAL_OPERATIONAL	0x5	Node is at normal operational mode
Bit 6..0	STATUS_OPERATIONAL_IS_STOPPED	0x4	Node has stopped
Bit 6..0	STATUS_OPERATIONAL_HAS_BOOT_UP	0x0	Node has just boot up from power on

C functions:
STATUS_CODE CANopen_Producer_HEARTBEAT_Transmit_Heartbeat(CANopen *canopen); / STATUS_CODE CANopen_Consumer_HEARTBEAT_Receive_Heartbeat(CANopen *canopen, uint8_t node_ID, uint8_t data[]);

GUARD
This is used if the server wants to send a request to the client and ask for an operational status. GUARD has the same data frame as HEARTBEAT, but the difference is when the server sends a GUARD request to a client, the client will answer the server with an operational status of the client. GUARD cannot be sent from master to the slave if HEARTBEAT is activated at the slave, due to the same frame.

Also, when the server sends the GUARD request to the client, it measures how long it would take to get a response back from the slave. If the time is too long, then the server sends out an EMCY message.

Transmit command:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x700 + Node ID	0x0	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Response from the slave to the master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
0x700 + Node ID	Status	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Status	Enum in C code	Hex	Meaning
Bit 7	TOGGLE_HEARTBEAT_0	0x0	Bit changes for every time the C function calls
Bit 7	TOGGLE_HEARTBEAT_1	0x1	Bit changes for every time the C function calls
Bit 6..0	STATUS_OPERATIONAL_ENTER_PRE_OPERATIONAL	0x7F	Node has enter Pre-Operational mode
Bit 6..0	STATUS_OPERATIONAL_NORMAL_OPERATIONAL	0x5	Node is at normal operational mode
Bit 6..0	STATUS_OPERATIONAL_IS_STOPPED	0x4	Node has stopped
Bit 6..0	STATUS_OPERATIONAL_HAS_BOOT_UP	0x0	Node has just boot up from power on

C functions:
STATUS_CODE CANopen_Server_GUARD_Receive_Response_Guard(CANopen *canopen, uint8_t node_ID, uint8_t data[]); / STATUS_CODE CANopen_Server_GUARD_Transmit_Request_Guard(CANopen *canopen, uint8_t node_ID); / STATUS_CODE CANopen_Client_GUARD_Receive_Request_Guard(CANopen *canopen, uint8_t node_ID); / STATUS_CODE CANopen_Client_GUARD_Transmit_Response_Guard(CANopen *canopen, uint8_t node_ID);

NMT
This is used if the master will enable, disable, restart or reset communication for a slave node. For every command NMT sends out, then the slaves will respond with a heartbeat if the heartbeat is disabled. All nodes always transmit a heartbeat when a node enters into pre-operational state.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Node ID	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	NMT_MASTER_TO_SLAVE	0x0	Transmit from master to slave
CS	CS_START_REMOTE_NODE	0x1	Enable all services
CS	CS_STOPT_REMOTE_NODE	0x2	Disable all services except NMT and HEARTBEAT
CS	CS_ENTER_PRE_OPERATIONAL	0x80	Only disable PDO service
CS	CS_RESET_NODE	0x81	Vad gör denna?
CS	CS_RESET_COMMUNICATION	0x82	Vad gör denna?

Response from slave to master: Heartbeat
C functions:
void CANopen_Master_NMT_Transmit_Service_Operation(uint8_t cs, uint8_t node_id);

LSS
The services of the LSS protocol (Layer Settings Services) are used to assign the node-ID and/or the baud rate of the controller directly via the CANopen bus. This is especially useful with devices that have no means for the mechanical configuration (e.g., rotary switches) of the parameters.

The LSS protocol requires a CANopen device in the network that performs the role of the LSS master. All other devices have the role of the LSS slave.

Each LSS slave is equipped with a unique LSS address that consists of the four 32-bit entries of the Identity Object 0x1018.

An LSS slave may either be in configuration mode or in wait mode. The LSS master is responsible for switching between the two modes. Some LSS services (Configuration, Inquiry) are only available in configuration mode.

All messages of the LSS protocol consist of 8 bytes, whereby byte 0 always contains the Command Specifier (CS) of the service.
Two CAN IDs are reserved for the LSS protocol:
- 0x7E5: For the messages from the LSS master to the LSS slaves (request)
- 0x7E4: For the messages from the LSS slaves to the LSS master (response)
Switch Mode Global Protocol
With this service, the LSS master switches all LSS slaves in the network to configuration mode or to wait mode.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Mode	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_SWITCH_MODE_GLOBAL_PROTOCOL	0x4	Enable or disable LSS
Mode	MODE_WAITING	0x0	LSS configuration OFF
Mode	MODE_CONFIGURATION	0x1	LSS configuration ON

Response from slave to master: No response back.
C functions:
void CANopen_Master_LSS_Transmit_Request_Switch_Mode_Global_Protocol(uint8_t mode); / static void CANopen_Slave_LSS_Receive_Request_Switch_Mode_Global_Protocol(CANopen *canopen, uint8_t data[]);

Switch mode selective protocol
This is used if the master wants to set vendor ID, product code, revision number and serial number to the identity object at the slaves. The value must be an unsigned 32-bit value. That means for example, vendor ID can have the value from 0x0 to 0xFFFFFFFF.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Value LSB Value MSB				0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_SWITCH_MODE_SELECTIVE_PROTOCOL_VENDOR_ID	0x40	Set vendor ID
CS	CS_SWITCH_MODE_SELECTIVE_PROTOCOL_PRODUCT_CODE	0x41	Set product code
CS	CS_SWITCH_MODE_SELECTIVE_PROTOCOL_REVISION_NUMBER	0x42	Set revision number
CS	CS_SWITCH_MODE_SELECTIVE_PROTOCOL_SERIAL_NUMBER	0x43	Set serial number

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_RECEIVE	0x7E4	Transmit from slave to master
CS	CS_SWITCH_MODE_SELECTIVE_PROTOCOL_RESPONSE	0x44	Response message

C functions:
STATUS_CODE CANopen_Master_LSS_Transmit_Switch_Mode_Selective_Protocol(CANopen *canopen, uint8_t cs, uint32_t value); STATUS_CODE CANopen_Slave_LSS_Transmit_Command_Specifier_(uint8_t cs);

Configure Node ID Protocol
This is used if the master wants to set node ID to the slaves. Node ID is the address of the device on the CAN network. Node ID can be from 0x1 to 0x7F only because node ID 0x0 is the master address.When you set the node ID, then you will get a status message back.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Node ID	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_CONFIGURE_NODE_ID_PROTOCOL	0x11	Set node ID

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Status code	Status code specific	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_RECEIVE	0x7E4	Transmit from slave to master
CS	CS_CONFIGURE_PROTOCOL_NODE_ID	0x11	Response message
Status code	STATUS_CODE_SUCCESSFULLY_COMPLETED	0x0	Parameter OK
Status code	STATUS_CODE_INVALID_PARAMETER	0x1	Parameter invalid
Status code	STATUS_CODE_APPLICATION_SPECIFIC	0xFF	Read the status code specific

C functions:
void CANopen_Master_LSS_Transmit_Configure_Node_Id_Protocol(CANopen *canopen, uint8_t node_id); void CANopen_Slave_LSS_Transmit_Status_Response(uint8_t cs, uint8_t status_code, uint8_t status_code_specific);

Configure Bit Timing Parameters Protocol
This is used if the master wants to set the baud rate to the slaves. Notice that this only configures the baud rate, not activates the baud rate.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Table selector	Table index	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_CONFIGURE_BIT_TIMING_PARAMETERS_PROTOCOL	0x13	Set baud rate
Table selector	TABLE_SELECTOR_0	0x0	Standard CiA baudrate table
Table index	TABLE_INDEX_BAUD_RATE_1000_KBS	0x0	1000 kB/s baudrate
Table index	TABLE_INDEX_BAUD_RATE_800_KBS	0x1	800 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_500_KBS	0x2	500 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_250_KBS	0x3	250 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_125_KBS	0x4	125 kB/s baudrate
Table index	TABLE_INDEX_BAUD_RATE_100_KBS	0x5	100 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_50_KBS	0x6	50 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_20_KBS	0x7	20 kB/s baud rate
Table index	TABLE_INDEX_BAUD_RATE_10_KBS	0x8	10 kB/s baud rate

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Status code	Status code specific	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E4	Transmit from slave to master
CS	CS_CONFIGURE_BIT_TIMING_PARAMETERS_PROTOCOL	0x13	Response message
Status code	STATUS_SUCCESSFULLY_COMPLETED	0x0	Parameter OK
Status code	STATUS_INVALID_PARAMETER	0x1	Parameter invalid
Status code	STATUS_APPLICATION_SPECIFIC	0xFF	Read the status code specific

C functions:
void CANopen_Master_LSS_Transmit_Configure_Bit_Timing_Parameters_Protocol(CANopen *canopen, uint8_t node_id); void CANopen_Slave_LSS_Transmit_Status_Response(uint8_t cs, uint8_t status_code, uint8_t status_code_specific);

Activate Bit Timing Parameters Protocol
This is used if the master wants to activate the given baud rate to the slaves with a switch delay time. Switch delay in milliseconds can be from 0x0 to 0xFFFF.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Delay ms LSB	Delay ms MSB	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_ACTIVATE_BIT_TIMING_PARAMETERS_PROTOCOL	0x15	Activate baud rate

Response from slave to master: No response back.
C functions:
void CANopen_Master_LSS_Transmit_Activate_Bit_Timing_Parameters_Protocol(uint16_t delay);

Store Configuration Protocol
This is used if the master wants the slaves to save its own LSS parameters in flash, harddrive, memory card etc.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_STORE_CONFIGURATION_PROTOCOL	0x17	Save LSS settings

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Status code	Status code specific	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS_SLAVE_TO_MASTER	0x7E4	Transmit from slave to master
CS	CS_STORE_CONFIGURATION_PROTOCOL	0x17	Response message
Status code	STATUS_SUCCESSFULLY_COMPLETED	0x0	Parameter OK
Status code	STATUS_INVALID_PARAMETER	0x1	Parameter invalid
Status code	STATUS_APPLICATION_SPECIFIC	0xFF	Read the status code specific

C functions:
void CANopen_Master_LSS_Transmit_Command_Specifier_Response(CANopen *canopen, uint8_t cs); void CANopen_Slave_LSS_Transmit_Status_Response(uint8_t cs, uint8_t status_code, uint8_t status_code_specific);

Inquire Identity Protocol
This is used if the master wants information about the slaves. It can be for example vendor ID, product code, revision number, serial number or node ID. When the master inquires one of these values, then the slaves respond with an unsigned 32-bit value back to the master.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	FUNCTION_CODE_LSS_TRANSMIT	0x7E5	Transmit from master to slave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_VENDOR_ID	0x5A	Ask for vendor ID from slave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_PRODUCT_CODE	0x5B	Ask for product code from slave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_REVISION_NUMBER	0x5C	Ask for revision number from slave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_SERIAL_NUMBER	0x5D	Ask for serial number from slave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_NODE_ID	0x5E	Ask for node ID from slave

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Value LSB Value MSB				0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS_SLAVE_TO_MASTER	0x7E4	Transmit from slave to master
CS	CS_INQUIRE_IDENTITY_PROTOCOL_VENDOR_ID	0x5A	Send vendor ID to master
CS	CS_INQUIRE_IDENTITY_PROTOCOL_PRODUCT_CODE	0x5B	Send product code to master
CS	CS_INQUIRE_IDENTITY_PROTOCOL_REVISION_NUMBER	0x5C	Send revision number to master
CS	CS_INQUIRE_IDENTITY_PROTOCOL_SERIAL_NUMBER	0x5D	Send serial number toslave
CS	CS_INQUIRE_IDENTITY_PROTOCOL_NODE_ID	0x5E	Send node ID to master

C functions:
void CANopen_Master_LSS_Transmit_Command_Specifier_Response(CANopen *canopen, uint8_t cs); void CANopen_Slave_LSS_Transmit_Identity_Protocol(uint8_t cs, uint32_t value);

Identity Remote Slave Protocol
This is used if the master wants to check if there exist nodes at the CAN network that have a specific value. Also there is an ability to check if there exists a node at the CAN network that has a low and a high value, so the master can identify with a certain range.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	Value LSB Value MSB				0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS MASTER_TO_SLAVE	0x7E5	Transmit from master to slave
CS	CS_IDENTITY_REMOTE_SLAVE_VENDOR_ID_PROTOCOL	0x46	Check if vendor ID exist
CS	CS_IDENTITY_REMOTE_SLAVE_PRODUCT_CODE_PROTOCOL	0x47	Check if product code exist
CS	CS_IDENTITY_REMOTE_SLAVE_REVISION_NUMBER_LOW_PROTOCOL	0x48	Check if revision number or lower exist
CS	CS_IDENTITY_REMOTE_SLAVE_REVISION_NUMBER_HIGH_PROTOCOL	0x49	Check if revision number or higher exist
CS	CS_IDENTITY_REMOTE_SLAVE_SERIAL_NUMBER_LOW_PROTOCOL	0x4A	Check if serial number or lower exist
CS	CS_IDENTITY_REMOTE_SLAVE_SERIAL_NUMBER_HIGH_PROTOCOL	0x4B	Check if serial number or higher exist

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS_SLAVE_TO_MASTER	0x7E4	Transmit from slave to master
CS	CS_IDENTIFY_REMOTE_SLAVE_PROTOCOL_RESPONSE	0x4F	Response message

C functions:
void CANopen_Master_LSS_Transmit_Identity_Remote_Slave_Protocol(CANopen *canopen, uint8_t cs, uint32_t value); void CANopen_Slave_LSS_Transmit_Command_Specifier_Response(uint8_t cs);

Identify Non Configured Remote Slave Protocol
This is used if the master wants to check if there exist nodes at the CAN network that have a node ID = 0xFF. 0xFF is the error address.

Command from master to slave:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS MASTER_TO_SLAVE	0x7E5	Transmit from master to slave
CS	CS_IDENTITY_NON_CONFIGURED_REMOTE_SLAVE_PROTOCOL	0x4C	Check if a node have address 0xFF

Response from slave to master:
COB ID	Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
COB	CS	0x0	0x0	0x0	0x0	0x0	0x0	0x0

Type	Enum in C code	Hex	Meaning
COB	LSS_SLAVE_TO_MASTER	0x7E4	Transmit from slave to master
CS	CS_IDENTITY_NON_CONFIGURED_REMOTE_SLAVE_PROTOCOL_RESPONSE	0x50	Response message

C functions:
void CANopen_Master_LSS_Transmit_Command_Specifier_Response(CANopen *canopen, uint8_t cs); void CANopen_Slave_LSS_Transmit_Command_Specifier_Response(uint8_t cs);